Sarah Cooley & Rob McGuire-Dale
cs/ece472
4 November 2009

Project 3

Testing the base processor model

Instruction changing every clock cycle
PC and PC next incremented by 4 each clock cycle
Reset pulled up for one clock cycle

Code Modifications Attached

mips_single.v

//-----------------------------------------------------------------------------
// Title : MIPS Single-Cycle Processor
// Project : ECE 313 - Computer Organization
//-----------------------------------------------------------------------------
// File : mips_single.v
// Author : John Nestor <nestorj@lafayette.edu>
// Organization : Lafayette College
//
// Created : October 2002
// Last modified : 6 November 2009 by Sarah Cooley and Rob McGuire-Dale
//-----------------------------------------------------------------------------
// Description :
// "Single Cycle" implementation of the MIPS processor subset described in
// Section 5.4 of "Computer Organization and Design, 3rd ed."
// by David Patterson & John Hennessey, Morgan Kaufmann, 2004 (COD3e).
//
// It implements the equivalent of Figure 5.19 on page 309 of COD3e
//
//-----------------------------------------------------------------------------

module mips_single(clk, reset);
    input clk, reset;

    // instruction bus
    wire [31:0] instr;

    // break out important fields from instruction
    wire [5:0] opcode, funct;
    wire [4:0] rs, rt, rd, shamt;
    wire [15:0] immed;
    wire [31:0] extend_immed, b_offset;
    wire [25:0] jumpoffset;

    assign opcode = instr[31:26];
    assign rs = instr[25:21];
    assign rt = instr[20:16];
    assign rd = instr[15:11];
    assign shamt = instr[10:6];
    assign funct = instr[5:0];
    assign immed = instr[15:0];
    assign jumpoffset = instr[25:0];

    //shift jumpoffset left 2 for jumpaddress
    assign jumpaddr = jumpoffset << 2;

 // sign-extender
    assign extend_immed = { {16{immed[15]}}, immed };

    // branch offset shifter
    assign b_offset = extend_immed << 2;

    // datapath signals
    wire [4:0] rfile_wn;
    wire [31:0] rfile_rd1, rfile_rd2, rfile_wd, alu_b, alu_out, b_tgt, pc_next,
        pc_int, pc, pc_incr, br_add_out, dmem_rdata;

    // control signals
    // Added control signals for bne and jump
    wire RegWrite, Branch, PCSrc, RegDst, MemtoReg, MemRead, MemWrite, ALUSrc,
Zero, Jump, BranchNE;

    wire [1:0] ALUOp;
    wire [2:0] Operation;

    // module instantiations
    reg32	PC(clk, reset, pc_next, pc);

    add32	PCADD(pc, 32'd4, pc_incr);
    add32	BRADD(pc_incr, b_offset, b_tgt);
    // Does the PC addition for jump
    add32	JUMPADD(jumpaddr, pc_incr, jumpaddr);

 reg_file	RFILE(clk, RegWrite, rs, rt, rfile_wn, rfile_rd1, rfile_rd2, rfile_wd);

 alu	ALU(Operation, rfile_rd1, alu_b, alu_out, Zero);

    alu_ctl	ALUCTL(ALUOp, funct, Operation);

    rom32	IMEM(pc, instr);

    mem32	DMEM(clk, MemRead, MemWrite, alu_out, rfile_rd2, dmem_rdata);

    and	BR_AND(PCSrc, Branch, Zero);
    and	BRNE_AND(PCSrc, (Branch & Zero), (BranchNE & !(Zero)));

mux2 #(5)	RFMUX(RegDst, rt, rd, rfile_wn);

    mux2 #(32)	PCMUX(PCSrc, pc_incr, b_tgt, pc_int);

    mux2 #(32)	ALUMUX(ALUSrc, rfile_rd2, extend_immed, alu_b);

    //The MUX that handles
    mux2 #(32)	JMUX(Jump, pc_intmdt, jumpaddress, pc_next);

    mux2 #(32)	WRMUX(MemtoReg, alu_out, dmem_rdata, rfile_wd);

    control_single CTL(.opcode(opcode), .RegDst(RegDst), .ALUSrc(ALUSrc),
.MemtoReg(MemtoReg), .RegWrite(RegWrite), .MemRead(MemRead),
.MemWrite(MemWrite), .Branch(Branch), .ALUOp(ALUOp), .Jump(Jump),
.BranchNE(BranchNE));
endmodule
control_single.v

//-----------------------------------------------------------------------------
// Title : MIPS Single-Cycle Control Unit
// Project : ECE 313 - Computer Organization
//-----------------------------------------------------------------------------
// File : control_single.v
// Author : John Nestor <nestorj@lafayette.edu>
// Organization : Lafayette College
//
// Created : October 2002
// Last modified : 6 November 2009 by Sarah Cooley and Rob McGuire-Dale
//-----------------------------------------------------------------------------
// Description :
// Control unit for the MIPS "Single Cycle" processor implementation described
// Section 5.4 of "Computer Organization and Design, 3rd ed."
// by David Patterson & John Hennessey, Morgan Kaufmann, 2004 (COD3e).
//
// It implements the function specified in Figure 5.18 on p. 308 of COD3e.
//
//-----------------------------------------------------------------------------

module control_single(opcode, RegDst, ALUSrc, MemtoReg, RegWrite, MemRead, MemWrite, Branch, BranchNE, Jump, ALUOp);
    input [5:0] opcode;

// Add Jump and BranchNE to outputs
    output RegDst, ALUSrc, MemtoReg, RegWrite, MemRead, MemWrite, Branch, BranchNE, Jump;
    output [1:0] ALUOp;
    reg RegDst, ALUSrc, MemtoReg, RegWrite, MemRead, MemWrite, Branch, BranchNE, Jump;
    reg [1:0] ALUOp;

 // Add J, ADDI, and BNE to our instructions and codes
    parameter R_FORMAT = 6'd0;
    parameter LW = 6'd35;
    parameter SW = 6'd43;
    parameter BEQ = 6'd4;
    parameter BNE = 6'd5;
    parameter J = 6'd2;
    parameter ADDI = 6'd8;

 //Added Control Signals for BEQ, J, and ADDI based on numbers from the book
    always @(opcode)
    begin
        case (opcode)
        R_FORMAT :
        begin
        RegDst=1'b1;
  ALUSrc=1'b0;
  MemtoReg=1'b0;
  RegWrite=1'b1;
  MemRead=1'b0;
        MemWrite=1'b0;
  Branch=1'b0;
  BranchNE = 1'b0;
  Jump = 1'b0;
  ALUOp = 2'b10;
        end

 LW :
        begin
        RegDst=1'b0;
 ALUSrc=1'b1;
 MemtoReg=1'b1;
 RegWrite=1'b1;
 MemRead=1'b1;
        MemWrite=1'b0;
 Branch=1'b0;
 BranchNE = 1'b0;
 Jump = 1'b0;
 ALUOp = 2'b00;
        end

 SW :
        begin
        RegDst=1'bx;
 ALUSrc=1'b1;
 MemtoReg=1'bx;
 RegWrite=1'b0;
 MemRead=1'b0;
        MemWrite=1'b1;
 Branch=1'b0;
 BranchNE = 1'b0;
 Jump = 1'b0;
 ALUOp = 2'b00;
        end

 BEQ :
        begin
        RegDst=1'bx;
 ALUSrc=1'b0;
 MemtoReg=1'bx;
 RegWrite=1'b0;
 MemRead=1'b0;
        MemWrite=1'b0;
 Branch=1'b1;
 BranchNE = 1'b0;
 Jump = 1'b0;
 ALUOp = 2'b01;
        end

BNE :
 begin
RegDst=1'bx;
ALUSrc=1'b0;
MemtoReg=1'bx;
RegWrite=1'b0;
MemRead=1'b0;
       MemWrite=1'b0;
Branch=1'b0;
BranchNE = 1'b1;
Jump = 1'b0;
ALUOp = 2'b01;
 end

J :
 begin
RegDst=1'bx;
ALUSrc=1'b0;
MemtoReg=1'bx;
RegWrite=1'bx;
MemRead=1'bx;
       MemWrite=1'bx;
Branch=1'b1;
BranchNE = 1'b0;
Jump = 1'b1;
ALUOp = 2'b01;

 end

ADDI :
 begin
RegDst=1'b1;
ALUSrc=1'b0;
MemtoReg=1'b0;
RegWrite=1'b1;
MemRead=1'b0;
       MemWrite=1'b0;
Branch=1'b0;
BranchNE = 1'b0;
Jump = 1'b0;
ALUOp = 2'b10;
 end

       default
       begin
        $display("control_single unimplemented opcode %d", opcode);
        RegDst=1'bx; ALUSrc=1'bx; MemtoReg=1'bx; RegWrite=1'bx; MemRead=1'bx;
        MemWrite=1'bx; Branch=1'bx; ALUOp = 2'bxx;
       end

       endcase
    end
endmodule